## Slide 1: Spiking Neural Network RTL Design and Verification Using System Verilog & UVM Methodology
By
Gaurang Brijbhushan Pandey
BITS ID : 2023HT80003 MTech Microelectronics 2023-25

## Slide 2
Agenda
Introduction to AI & Machine Learning
Hardware vs. Software Implementation
Introduction to Spiking Neural Networks (SNNs)
SNN RTL Design Architecture
  System Overview
  Key Components
Verification Methodology using UVM
  Testbench Architecture
  Verification Components
Project Implementation & Results
Conclusion

## Slide 3: Introduction to AI & Machine Learning
Artificial Intelligence: Systems that can perform tasks that typically require human intelligence
  Problem-solving, pattern recognition, decision making
  Revolutionary impact across industries
Machine Learning: Subset of AI focused on algorithms that improve through experience
  Supervised, unsupervised, and reinforcement learning
  Neural networks, deep learning, convolutional networks
Industry Growth: Expected to reach $407 billion by 2027
  Exponential increase in AI applications
  Growing computational demands

## Slide 4: The AI Computational Challenge
Growing Model Complexity:
  GPT-4: 1.76 trillion parameters
  Increasing accuracy demands more compute power
Energy Consumption Concerns:
  Training large models can emit as much carbon as 5 cars over their lifetime
  Data centers account for 1-2% of global electricity use
Real-time Processing Requirements:
  Edge computing demands low-latency solutions
  Autonomous vehicles, medical devices need instant responses

## Slide 5: Hardware vs. Software Implementation
Software Implementation
  Advantages:
  Flexibility and ease of development
  Rapid prototyping and iteration
  Lower initial investment
  Limitations:
  Performance overhead from general-purpose architecture
  Power inefficiency
  Serial processing bottlenecks
Hardware Implementation
  Advantages:
  10-100x performance improvement
  Superior energy efficiency
  Parallel processing capabilities
  Lower latency for real-time applications
  Limitations:
  Expensive

## Slide 6: Why Hardware Acceleration Matters
Performance Comparison
Real-world Impact: Tesla FSD Computer: 144 TOPS performance
Google TPU: 180 teraflops, 90x more efficient than CPUs
Neuromorphic chips: IBM TrueNorth - 1 million neurons with only 70mW power

## Slide 7: Introduction to Spiking Neural Networks
Bio-inspired Computing:
  Mimics biological neurons that communicate through discrete "spikes"
  Event-driven computation
Key Features:
  Temporal information processing
  Energy efficiency through sparse activation
  Asynchronous processing
Applications:
  Edge computing devices
  Pattern recognition
  IoT solutions requiring low power

## Slide 8: Project Scope and Objectives
Design a multi-layer SNN core at RTL level:
  Spike-based computations
  Synaptic weight updates
  Multi-layer spike propagation
Develop UVM-based verification environment:
  Functional correctness verification
  Accurate inter-layer spike propagation
Measure performance metrics:
  Correctness, Code coverage
  Latency & Functional Coverage is not in the current scope
Explore real-world applications:
  Pattern recognition
  Low-power computation

## Slide 9: SNN RTL Design: System Overview
Architecture Components:
  Input layer that converts pixel values to spike trains
  Hidden layer with configurable neurons
  Output layer that produces classification results
  Control and status registers (CSRs) via APB interface
  Clock division and reset synchronization
Processing Model:
  Binary spikes mimic biological neural networks
  Event-driven computation

## Slide 10: SNN Top-Level Architecture

## Slide 11: SNN Components: Input Processor
Purpose:
  Converts input values (0-255) into spike trains
  Implements rate coding for neural inputs
Operation:
  Uses counters to control spike generation timing
  Computes dynamic thresholds based on pixel values
  Generates output spikes when counters are below thresholds
Interface:
  Clock and reset signals
  Pixel value inputs
  Generated spike train outputs

## Slide 12: SNN Components: Leaky Integrate-and-Fire Neuron
Core Computational Unit:
  Implements biological neuron behavior
  Accumulates weighted spikes
  Applies decay factor (leakage) – Not implemented in the current design
  Fires when threshold is exceeded
Key Parameters:
  Membrane potential (32-bit)
  Configurable leak factor – No dedicated CSRs
  Firing threshold – Programmable CSR
  Reset behavior

## Slide 13: SNN Components: Synapse Module
Function:
  Spike-weight multiplication
  Transmits weighted signals to neurons
  Key for learning through weight adjustment
  Programable CSRs for weight and spike threshold
Operation:
  Accumulates weighted input spikes
  Compares accumulated value to threshold
  Generates output spikes when threshold exceeded
  Resets after configurable spiking window

## Slide 14: SNN Components: Neuron Layer
Structure:
  Groups multiple LIF neurons & synapses
  Forms functional network layer
  Handles parallel spike processing
  Feed OR-ed input (outputs from synapses) to the neurons
Connectivity:
  Fully connected between inputs and neurons
  Aggregates weighted spikes for each neuron
  Produces output spikes from each layer

## Slide 15: SNN Control: CSR and Interface
APB Interface:
  External configuration access
  Memory-mapped registers
Configurable Parameters:
  Synaptic weights
  Neuron thresholds
  Spike thresholds
  Control registers
Clock and Reset Management:
  Clock divider for controlled timing
  Reset synchronization across domains

## Slide 16: Verification Strategy: UVM-Based Approach
Objective:
  Verify SNN functional correctness
  Ensure configuration flexibility
  Validate spike propagation accuracy – Input to Output connectivity
Methodology:
  Universal Verification Methodology (UVM)
  Layered testbench architecture
  Reusable verification components

## Slide 17: Verification Architecture

## Slide 18: Verification Components: APB Agent
Purpose:
  Drive APB-based CSR accesses
  Configure SNN parameters
Components:
  Transactions for address, data, control
  Driver for bus operations
  Monitor for tracking bus activity
  Register model adapter and predictor

## Slide 19: Verification Components: SNN Agent
Function:
  Handle pixel input driving
  Capture neuron spike outputs
Components:
  Transactions for pixel data
  Driver for 8-bit input array [64 indexes wide]
  Monitor for spike output observation
  Sequencer for coordinating test patterns

## Slide 20: Verification: Register Model and Scoreboard
Register Abstraction Layer:
  Models design registers and fields (UVM RAL Model)
  Enables consistent access and verification (Register Write/Read APIs)
  Front door and backdoor access support
Scoreboard:
  Verifies output spike correctness
  Compares expected vs. actual behavior

## Slide 21: Verification: Test Scenarios
Stimulus Patterns:
  Register bit-bash and random access
  Random pixel values
  Reset Scenario
  Gradient and checkered patterns
  Noise injection tests
Verification Focus:
  Functional correctness
  Reset behavior
  Pattern recognition capability
  Stability under varying inputs

## Slide 22: Verification: Waveform Snapshot
CSR WRITE READ OPERATION via APB

## Slide 23: Verification: Waveform Snapshot
 INPUT - Drive Pixel Values
OUTPUT SPIKES 

## Slide 24: Verification: Code Coverage

## Slide 25: Potential Applications & Future Work
Real-world Applications:
  Energy-efficient edge computing
  Pattern recognition in resource-constrained environments
  Neuromorphic sensor processing
  Autonomous systems
Future Extensions:
  Multi-core SNN scaling
  Hardware optimization for FPGA/ASIC
  Integration with sensor interfaces
  Functional Coverage and Power Consumption
  Netlist to GDS II flow

## Slide 26: Conclusion
Successfully designed and verified a configurable SNN in SystemVerilog RTL
Implemented bio-inspired neuromorphic computation with hardware efficiency
Created robust verification methodology using UVM
Demonstrated potential for real-world neuromorphic computing applications
Established foundation for future hardware-based AI acceleration research

## Slide 27: GitHub Repository: https://github.com/gaurangp130693/SNN-Project

## Slide 28: Thank You
Dissertation by: Gaurang Brijbhushan Pandey
BITS ID: 2023HT80003
Degree Program: M Tech (Microelectronics)
Supervisor: Kishan Kalavadiya